## Slide 1: Einstein TurtleBot
Scott Matsuo and Philip Arola

## Slide 2: Overview/Goals/Requirements
Robot must have some simple body gestures like greeting, hello, good bye, shake hand, etc.
Robot must have some vision capabilities: recognize human face (not who this person is, only that human is present and where) , recognize object (like big red box or yellow round object etc), or recognize another robot (which one).
Robot must use some type of Machine Learning, Evolutionary algorithm, neural net or fuzzy logic.

## Slide 3: ROS Project
The project is divided into 4 nodes:
Dynamixel servo initialization
Servo control
Face detection
Gesture control

## Slide 4: Servo Setup/Config/research
 | ID | Min | Max | Torque | Min | Max | Range | Init | Min | Max | Min (rad) | Max (rad) | Description
Right Arm | 1 | 409.20 | 818.40 | 400 | 120 | 240 | 120 | 409 | 409 | 819 | 0.00 | 2.52 | Shoulder Vertical
2 | 341.00 | 647.90 | 400 | 100 | 190 | 90 | 341 | 341 | 648 | 0.00 | 1.89 | Shoulder Horizontal
3 | 306.90 | 716.10 | 400 | 90 | 210 | 120 | 306 | 306 | 717 | 0.00 | 2.52 | Elbow Vertical
4 | 341.00 | 647.90 | 400 | 100 | 190 | 90 | 341 | 341 | 648 | 0.00 | 1.89 | Elbow Horizontal
Left Arm | 5 | 204.60 | 613.80 | 400 | 60 | 180 | 120 | 204 | 204 | 614 | 0.00 | 2.52 | Shoulder Vertical
6 | 341.00 | 647.90 | 400 | 100 | 190 | 90 | 341 | 341 | 648 | 0.00 | 1.89 | Shoulder Horizontal
7 | 613.80 | 1023.00 | 400 | 180 | 300 | 120 | 613 | 613 | 1023 | 0.00 | 2.52 | Elbow Vertical
8 | 409.20 | 682.00 | 400 | 120 | 200 | 80 | 409 | 409 | 682 | 0.00 | 1.68 | Elbow Horizontal
Head | 9 | 358.05 | 664.95 | 400 | 105 | 195 | 90 | 511 | 358 | 665 | -0.94 | 0.95 | Neck Horizontal
10 | 375.10 | 613.80 | 400 | 110 | 180 | 70 | 375 | 375 | 614 | 0.00 | 1.47 | Neck Vertical
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
Raise Right Arm | 2.52 | 0.95 | 1.05 | 1.05 | 2.52 | 1.89 | 1.05 | 0 | 0 | 0.8 |  |  | 
Raise Left Arm | 0 | 0 | 1.05 | 1.89 | 0 | 0.84 | 1.05 | 0 | 0 | 0.8 |  |  | 
Notes: 10 Total Servos, each is controlled individually, range is limited to prevent damage, played with init value so head is in middle at 0

## Slide 5: Vision
Using the default OpenCV Haar Cascade Classifier, we find faces and their location in the image
The amount of faces, and their locations, are published on a ROS topic
If a monitor is attached, we display the image, along with the faces recognized
  We also display the zone where faces trigger a gesture response on screen

## Slide 6: Putting them together
This is where ROS comes in for our project. We used two topics that publish from the face detection script to send over how many faces there are, and where they are
The gesture code interprets these, and determines which gesture methods to call
Each gesture method is a fairly straightforward function that publishes target servo values, then waits, the sends the next values (wash, rinse, repeat).

## Slide 7: Challenges (of the technical nature)
Wires disconnect when robot moves sometimes, bring the whole dynamixel bus down
  Replacing wires helps, but this is a never-ending hunt
Navigating and creating ROS/Catkin projects was a learning experience
Configuring development devices, and making sure that we can work across multiple devices

## Slide 8: What we learned, what we would do differently
Add more gestures/have it robot respond accordingly to distance
Have different gestures behave differently on the meta level; stack gestures so one can execute, and then another can midway through (eg: rotate torso, then wave)
Refine facial detection for less false positives (eyes are seen as faces within faces) and less false negatives (head rotation relative to camera is the worst culprit)

## Slide 9: In Conclusion
This was an awesome project more like this please

## Slide 10: Media